## Slide 1: Istio IPv6 Proof of Concept
Paul Michali
Principal S/W Engineer
3/20/2018
Using multi-node, bare-metal cluster

## Slide 2: GOAL: Identify Istio IPv6 Readiness
Check basic operation
Not intended to be exhaustive analysis
Minimum effort to get things working
Use as a starting point for adding support

## Slide 3: Background: Kubernetes IPv6
IPv6 only support (no dual-stack)
Uses DNS64/NAT64 for access to IPv4 only sites.
Reference Bridge plugin
Development setup options…
  KubeAdm (manually)
  Kubeadm-dind-cluster (DinD)
  Lazyjack (for bare-metal)

## Slide 4: What Was Done?
Kubernetes cluster on three bare-metal nodes (Lazyjack)
  v1.10.0-beta.2
  IPv6 only mode
  Using Bridge plugin
Used recent Istio from master (cloned March 5th)
Temporary changes (hacks) to Istio and sample apps

## Slide 5: Results?
Good
  It WORKS!
  Code changes were not very complicated
Bad
  Some small changes had huge effect on unit tests
  Numerous golden master files needed update
Ugly
  Some parts of Istio are not “ready” for IP mode flexibility

## Slide 6: Details
Demo of running setup
Audit of code (Issue 4087)
Issues created for issues seen during PoC:
  4095 (merged)
  4096 (in progress), 4097 (next up)
  4098-4102 (need community help!)

## Slide 7: Futures
Proposed approach for adding IPv6 support…
  Similar to Kubernetes, bottom up infrastructure changes to support IPv6
  Using audit as starting point, creating more issues as gaps found
  Once operational, add IPv6 specific E2E tests, and update docs
Decide whether IP mode determined by config, and/or dynamically
  Determine how to handle hard-coded items (templates, constants)
Try other plugins (e.g. Calico), load balancer (e.g. MetalLB), auth.
Dual stack!

## Slide 8: Reference Info
Blog on setting up your own IPv6 bare-metal cluster with Istio
  http://blog.michali.net/2018/02/19/lazyjack-provisioning-bare-metal-for-ipv6-kubernetes/
  http://blog.michali.net/2018/03/06/istio-on-ipv6-kubernetes-undiscovered-country/
Repo with the temporary changes for IPv6
  https://github.com/pmichali/istio/tree/ipv6
  https://github.com/pmichali/istio/commits/ipv6

## Slide 10: Physical Topology
Master
(bxb-c2-77)
Minion
(bxb-c2-78)
Minion
(bxb-c2-79)
Administrative Network/External Access
Management/Pod Networks

## Slide 11: Logical Topology
Master
DNS64
NAT64
Pod network fd00:40::/80
Support network fd00:10::/64
Admin network 10.86.7.64/26
Pvt Network 172.18.0.128/25
fd00:10::200
fd00:10::100
bridge
172.18.0.200
NAT44
fd00:10:64:ff9b::/96
Service net
fd00:30::/110
fd00:20::2
Management network fd00:20::/64